## Slide 1: Guidelines for Conducting Cable Blowing Tests
Willem Griffioen, Jan Jonker, Int. Wire & Cable Symp., Virtual, October 4-8, 2021

## Slide 2: Contents
Introduction
Resonances
  Blowing theory
  Examples
Blowing until end of duct
Recommendations for testing
  Constant blowing pressure
  Same end speed for all tests
Conclusions

## Slide 3: Introduction
Blowing tests important for characterisation of cable
Test trajectories in many shapes

## Slide 4: Introduction
Test trajectories above ground or underground
  Above ground less expensive
  Above ground thermal expansion (differences)
Bundles of microducts in ducts
  Single duct loop, bundle coupled in loops
  Multiple duct loops, microduct bundle uncut over entire length (can be changed easily)
Unwanted effects
  Undulations in (micro)ducts due to thermal expansion
  Resonances (strong variations in installation speed)
Tests done in different ways
  Not always end of trajectory is reached
  Sometimes speed is kept constant by varying pressure, sometimes pressure is kept constant

## Slide 5: Resonances
Blowing theory
  Force build-up:
Pressure gradient larger in duct part with cable
  Depends on filling degree (Dc / Dd)
  For 10 bar over 1500 m and filling degree 1/3:
  Blowing force proportional to dp/dx
  Today usually higher filling degree
  So, extreme filling effect
  Blowing force

## Slide 6: Resonances
Examples
  6 mm cable in 10/8 mm microduct
  Cable installed 25%, 50%, 75% and 100%
  Blowing force (= only cable part)
  Pressure (absolute!) at cable head:
  1.83, 1.34, 1.13 and 1.00 bar
Example 1
  Cable weight 0.32 N/m
  Cable stiffness 0.16 Nm2
  Coefficient of friction 0.06
  Red line is gravity friction
  Force build up calculated from front end cable

## Slide 7: Resonances
Example 2
  Same as example 1, but now coiled on drum
  Continuous bending radius 0.6 m
  Force starts with higher friction because of bending
  Strong capstan effect, explodes already for cable at 75%
Explanation resonances (for Example 2)
  Cable at inside facing duct wall is pushed to outside
  This is a hopping operation, hardly any sliding friction
  Goes layer by layer, to and fro in the layer, rattling!
  Until duct end, then upstream wave back by air drag
  Rattling really observed when blowing in coiled ducts
  Also observed: stop and go of pushing
  In counter phase of cable coming out

## Slide 8: Resonances
Example 3
  Test trajectory, loops of 100 m long
  Continuous curves (R = 6 m, γ = 74.4°)
  Total angle per loop 955°
  Advantage: thermal expansion accommodated
  Resonances may occur on such trajectories (as is observed in similar trajectories)
Example 4
  IEC trajectory, loops of 100 m long (IEC 60794-1-21 “Optical cable test procedures” Method E24)
  Long straight sections, sharper bends
  Total angle per loop 360°
  Pure friction in straights, no resonances

## Slide 9: Resonances
Example 4
  When the IEC trajectory is above ground, thermal expansion (differences) of the ducts might cause undulations, leading to poorer blowing performance
  This problem can be solved using “duct spanners”

## Slide 10: Blowing until end of duct
Why blowing until the end?
  Not only comparing cables
  Also obtaining the effective coefficient of friction, for simulations in practical trajectories
  Existing software does not take into account filling effect, can only handle uniform flow over length
  For cables with different diameter you cannot even compare cables when stopping before the end
  When cable cannot reach the end at acceptable pressure: cut back or disconnect loops
    And anticipate this well before the cable is reaching the end (enabling stationary airflow, see further)
Example: small cable and large cable, behaviour in same duct
  Small cable blows better (longer length possible)
  But when only a relatively short length can be reached for both, the larger cable might reach further because it picks up a relatively larger part of the pressure gradient
  Misleading!

## Slide 11: Recommendations for testing
Constant blowing pressure for testing
  Select constant blowing pressure
  Not too low, to be sure of turbulent flow and for accuracy of the test
  Not too high, so blowing out is also possible (about 20-30% more pressure needed because synergy of pushing force is lacking)
  Constant pressure to be sure of stationary flow (according to theory used for software)
    Note that time to reach stationary flow depends on geometric factors duct diameter, filling factor and length. The longer the lengths, the smaller the duct diameter and the larger the filling factor, the longer it takes
  Start with pushing first, then allow air (to avoid the cable being blown out of the machine)
  Adjust pressure to (anticipated) low end speed (e.g. 20 m/min) well before cable reaches the end
    If no suitable pressure is possible on trajectory length then cut back duct length (or decouple loops)

## Slide 12: Recommendations for testing
Same end speed for all tests
  Low but acceptable end speed (e.g. 20 m/min), that is how you would plan max distances
  Most machines do not correct for varying pushing force at differing speeds
  Dissipation in drive belts or wheels depends on cable speed
  Drum pay off force varies with speed
  Even coefficient of friction may depend on cable speed (especially when “thick” lubricant is used)

## Slide 13: Conclusions
Different blowing test trajectories and procedures compared
  Above ground trajectory costs less, but suffers from thermal expansion (solved by duct spanner)
  Test trajectories with continuous bends may accommodate thermal expansion, but resonances may occur
Qualitative explanation given of these resonances
  Such resonances are more clear (and defined, and spectacular) when installing with duct on drum
It has been argued why the cable shall always reach the end of the duct in blowing tests
It has been argued why constant air pressure is needed (at least close to end of the test)
It has been argued why a low but acceptable end speed (e.g. 20 m/min) is needed, same for all tests