## Slide 1: Blowing Cables in Ducts Fixed at Regular Intervals
Willem Griffioen, Int. Wire & Cable Symp., Providence (RI), 12 October 2020

## Slide 2: Contents
Introduction
Analysis
  Hanging of duct
  Temperature effects
  Effect of water
  Effect on blowing and floating distances
  Example with blowing
  Sag of cable
  Example with Floating
Conclusions

## Slide 3: Introduction
Installation of cables in ducts by blowing used worldwide more than 3 decades
  One step installation (no winch rope to install)
  Equipment and labor at one side of duct
    Low forces on cable, long lengths (record 5.3 km) Swissgrid AG and Engadiner Kraftwerke EKW, Switzerland
Floating (with water instead of air)
  Even longer lengths because of buoyancy (record 12.4 km)
    Nexans, Switzerland
Not many bends
No sharp bends
But: how straight is straight?

## Slide 4: Introduction
Duct fixed at regular intervals → sags → not straight
  Fixed on (tunnel) walls
  Fixed under bridges
  Held in place under water by blast-weights
Example 1
  Blowing (cascade) micoduct cables at CERN (record in 2004)
  Span 1.5 m
  Blowing distance 3.6 km reached!
Example 2
  Floating 20 mm cable (Switzerland)
  Span 1.5 m (laser aligned)
  Floating distance 12.4 km reached (still record today)

## Slide 5: Analysis: Hanging of duct
Model:
Stiffness dominated:
Force dominated (50 N):
In the middle of span d: Sag Sd
General: requires numerical calculation
Example HDPE 32/26 mm duct

## Slide 6: Analysis: Hanging of duct
Numerical solution for 50 N
Also other forces
Note:
Compressive force:
Asymptote cannot pass
buckling length b

## Slide 7: Analysis: Hanging of duct
Numerical solution for 50 N
Also other forces

## Slide 8: Analysis: Temperature effects
Temperature change → length changes
Length change → sag changes
Length change → also force changes
New equilibrium with new length, force and sag
Sag change → force changes

## Slide 9: Analysis: Temperature effects
Initial (mounting) situation
After temperature increase
Note the tensile and compressive zones left and right of blue line
Compressive:
Rapid increase of sag after buckling length b
  20 °C → 522 N → b = 1.32 m

## Slide 10: Analysis: Effect of water
Filling with water → weight changes
Weight change → sag changes
Sag change → force changes
Force change → length changes
Etcetera, new equilibrium established
Length change → sag changes

## Slide 11: Analysis: Effect of water
Initial (mounting) situation
After filling with water
After cooling with water

## Slide 12: Analysis: Effect on blowing and floating distances
Installation cable in duct with help of fluid drag
  Fluid is gas (air) → blowing
  Fluid is liquid (water) → floating
  Little sag and large free space cable in duct → Aeff can be zero
Undulation terms depending on span and sag:
  Period P = span d
  Effective amplitude Aeff depends on sag S and diameters cable and duct
direction change stiffness friction

## Slide 13: Analysis: Example with blowing (12 bar, 500 N pushing force)
Cable
  Diameter Dc = 20 mm
  Weight W = 3.2 N/m
  Stiffness B = 10 Nm2
Duct
  HDPE 32/26 mm from earlier example
  Coefficient of friction f = 0.08
Duct at initial conditions
  Blowing length decreases after 2 m span
  300 N tensile load → only small decrease
Duct after 20 °C temperature increase
  Sharp blowing length decrease after 1.32 m (buckling length at 20 °C temperature increase)

## Slide 14: Analysis: Sag of cable
Sag of 20 mm example cable ~ 3 times larger than sag 32/26 mm example duct (force zero)
  Cable will run over bottom duct with less sag than when not supported
  There will be no friction due to cable stiffness (as in earlier calculations)
  But, there is also friction due to dissipation cable continuously changing its curvature
    This is less than for full dissipation friction (as in cables pulled over rollers)
  However, the axial force in the cable is not zero and not related to the axial force in the duct
    Compressive close to blowing machine, tensile towards the end of the duct
  When floating the effective cable weight is less due to buoyancy
    Less sag of the sec cable (also more sag of the now heavier filled duct) so earlier calculations are more accurate
So, installation length depends on more parameters than treated in this paper, even though earlier calculations give a good idea (at least for floating)
Blowing and floating tests are recommended to confirm the presented theory in more detail than the few (successful) installations with blowing and floating

## Slide 15: Analysis: Example with floating (12 bar, > 500 N pushing force)
  Floating → buoyancy → less weight
  Extremely long installation lengths possible
  Calculated for Fc = 0 and zero cable speed
  Higher cable speed → higher pressure
  Needs higher pushing force because of “back pressure force” (377 N for 12 bar)
    With higher pressure 500 N easily consumed
    Justifies calculation with Fc = 0
  Example: 51.9 km when straight
    Local minimum L of 6.26 km at d of 2.4 m
    300 N pre-tension: L > 20 km (at 3 m) always
  Cooling by 20 °C
    Local minimum becomes hump or high, the latter 44.6 km
    Without pre-tension same L (~10.4 km) as uncooled for span d of 8 m

## Slide 16: Conclusions
Blowing
  Duct at constant temperature → blowing length hardly affected when span < 2 m
    When duct pre-tensioned at 300 N effect at higher span and even at 8 m only slight drop in blowing length
  Temperature increase can have large effect
    Blowing distance decreases by 1/3rd already at span above 1.32 m
    Combination of temperature variation and creep can be regarded as temperature increase
Floating
  Extremely long installation lengths reached, up to 51.9 km for span < 1.6 m
    Local minimum installation length of 6.26 km at span of 3 m
  Cooling of the duct by 20 °C by the flowing water increases installation length, worst case 10.4 km
Conclusions above for example of 20 mm cable in 32/26 mm duct
  Span scales proportionally to duct diameter and force scales to the square